## Slide 1
Current status of laser ionization at IGISOL and future concepts for the MARA recoil separator
Iain Moore
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Department of Physics, University of Jyväskylä, Finland

## Slide 2
The ion guide technique
- towards a more element-selective approach
Recent laser-related highlights (2013 – to date)
MARA – a vacuum-mode recoil mass separator
New concepts – a low-energy RIB facility at MARA
Outline of talk
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014

## Slide 3
The ion guide method
An ISOL system for ALL elements
Fast extraction (~ms)
Relatively low efficiency
Poor selectivity
Projectile source
Thin target
Mass separator
Ion guidance through
rf sextupole
Ion survival → ion guide method (non-selective)
Neutralization → laser re-ionization (Z selectivity)
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Notes: Universal, but for IGISOL we have a lot of isobaric contamination.
Low yields due to thin target.

## Slide 4
https://www.jyu.fi/fysiikka/en/research/accelerator/igisol
K=30 MeV
cyclotron
from K=130 MeV
cyclotron
IGISOL-4 – since 2013
Off-line ion sources:
(discharge, carbon cluster…)
Laser transport
for optical
manipulation/IRIS
Mass spectrometry
& post-trap spectroscopy
Collinear laser
spectroscopy
Laser ionization in-source/in-jet
Decay spectroscopy
(beam line not shown)
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
M. Reponen, Poster # PS1-C016
A. Jokinen, Plenary, Tuesday

## Slide 5
A more element-selective approach
First on-line in-gas-cell laser ionization (2013):
58Ni(p,n)58Cu (τ1/2=3.2 s)
Dual-chamber gas cell
Mass separator A=58
Lasers on/off 1 hour
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Total efficiency ~1%

## Slide 6
Gas jet laser ionization – how and why?
a quest for PURE radioactive ion beams
→ (the Laser Ion Source ``Trap´´)
I.D. Moore et al., AIP Conf. Proc. 831 (2006) 511
Yu. Kudryavtsev et al., NIMB 297 (2013) 7
2P3/2
2P1/2
2S1/2
Fj
Fi
an optimal environment for spectroscopy
(reduced temperature and pressure)
F=J+I
N
S
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Notes: Variation of LIST but using gas jet. Spectroscopy in jet.

## Slide 7
Free jet laser ionization in LIST geometry
63Cu
Vjet ~1040 m/s
FWHM = 3.9 GHz
FWHM = 6.7 GHz
FWHM = 1.8 GHz
Employ special nozzles
M. Reponen et al., NIMA 635 (2011) 24
Laser linewidth dominated
He, 180 mbar
I.D. Moore et al., NIMB 317 (2013) 208
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Notes: CoG difference from ref cell to jet is about 3 GHz which translates into a jet velocity of 1040 m/s.

## Slide 8
Fast piezo mirror
Fast-switched
photodiode
amplifier
Ti:sapphire crystal
d = n λcw
Lock-in Amplifier
(TEM Laselock)
PSD
HV
out
Input:
CW seed laser
1-100mW
Matisse TS Ti:sa
(100 kHz linewidth)
Output
pulsed, 30 ns width
2-5 W average power
20 MHz linewidth
pump laser
10-20 W, 10 kHz
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Development of narrowband pulsed
Ti:sapphire laser for gas-jet spectroscopy
V. Sonnenschein, Poster # PS2-C018
Notes: (hyperfine structure, isotope shifts) CW Ti:Sa seed enables a wide wavelength range

## Slide 9
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
First spectroscopy with the narrowband laser
Tested in Mainz to measure HFS of 227Ac (τ1/2=22 y)
Same transition applied by LISOL team, May 2014,
on 212-215Ac (see results in plenary talk, M. Huyse)
AI 46347.0 cm-1
J=5/2
22 801.1 cm-1
438.58 nm
J0=3/2
0 cm-1, 6d7s2
IP
424.7 nm
Future: measure 236-244Pu via in-jet RIS followed by high resolution
collinear laser spectroscopy (Mainz, Leuven, Manchester and Liverpool)
In-jet RIS in the search for 229mTh (new EU Horizon 2020 application)

## Slide 10
MARA: “Mass Analysing Recoil Apparatus”
Quadrupole triplet
Electrostatic deflector
Magnetic dipole
Focal plane
Beam
A new vacuum mode recoil separator
J. Sarén, PhD thesis, University of Jyväskylä (2011)
QQQED configuration
1st order resolving power ~260
Angular acceptance 10 msr
Advanced mass slit system
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
J. Uusitalo, Poster # PS2-C006
Notes: The combination of the ED and MD provides a fixed energy focus, the use of the QQQ results in the angular focus being at the same position as the energy focus. Focal plane may include a gas counter/Si detector. Almost all vacuum components have arrived, 6 month delay on the ED. Focal plane outside the cave to have access when beam is on target.
Two charge states delivered to focal plane

## Slide 11
A low-energy RIB facility at MARA
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
MR-TOF-MS funded and under design at IGISOL (T. Eronen)
24Mg(58Ni,2n)80Zr
Cross section 10 µb (C.J. Lister, 1987)
Total fusion-evap. ~500 mb
200 pnA, two charge states,
40 80Zr ions/s @ focal plane
Expect few atoms/s for in-jet RIS,
~10 ions/s at the MR-TOF-MS.

## Slide 12
“Day 1” experiments – heavy N~Z nuclei for the rp-process
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014
Mass measurements &
laser spectroscopy:
Region of N~Z 80Zr
Reion of N~Z 94Ag
Region of N~Z 100Sn
Combining experts from the IGISOL and nuclear spectroscopy groups, with external
support from Leuven. Providing a platform for testing novel devices for S3 at SPIRAL-2

## Slide 13
Thank you
IGISOL-laser team:
I. Pohjalainen, M. Reponen, V. Sonnenschein, A. Voss + IGISOL
MARA team
J. Uusitalo, J. Sarén, J. Partanen

## Slide 14
Inductively-heated hot cavity catcher (2014)
Development program towards production of N=Z 94Ag
487 MeV 107Ag21+
Variable Ni degrader foil
Pulse cyclotron,
measure extraction time
Heating coil
Primary beam
Mo crucible
SPIG
Variable Ni degrader foil
ARIS 2014, Advances in Radioactive Isotope Science, Tokyo, June1-6, 2014