## Slide 1: Studies on Nuclear Astrophysics and Exotic Structure at the Low-Energy RI beam Facility CRIB
Nuclear astrophysics group (CRIB supporting
members) in Center for Nuclear Study, Univ. of Tokyo:
Hidetoshi Yamaguchi (Lecturer),
Daid Kahl (Postdoc.)
Yuji Sakaguchi (Student)
with an Aid of Technical Staff:
N. Yamazaki (CRIB/Wien Filter), K. Yoshimura, M.Katayanagi, Y. Ohshiro (Hyper ECR ion source), S. Yamaka
in Collaboration with:
RIKEN, KEK, Kyushu, Tsukuba, Tohoku, Osaka, … (Japan)
McMaster (Canada), CIAE, IMP (China), Chung-Ang, Ehwa, SNU (Korea), INFN Padova/Catania (Italy), IOP(Vietnam) and others.

## Slide 2: Outline
Introduction of RI-beam facility “CRIB”.
    Cryogenic gas target for RI beam production.
Topics
  Resonant scattering experiments using thick-target method in inverse kinematics (TTIK).
  Active target (GEM-MSTPC):
  16N beta-delayed a decay experiment in Sep. 2013.
  Reaction mechanism study: 8B+Pb experiment in May 2014.

## Slide 3: CRIB
CNS Radio-Isotope Beam separator , operated by CNS (Univ. of Tokyo), located at RIBF (RIKEN Nishina Center).
  Low-energy(<10MeV/u) RI beams by in-flight method.
  Primary beam from K=70 AVF cyclotron.
  Momentum (Magnetic rigidity) separation by “double achromatic” system, and velocity separation by a Wien filter.
  Orbit radius: 90 cm, solid angle: 5.6 msr, momentum resolution: 1/850.

## Slide 4: CRIB in RIBF
AVF alone, operation cost ~1/10 of BigRIPS.
Ion source / AVF/ CRIB…have been developed under CNS-RIKEN collaboration (joint venture).
AVF

## Slide 5: Low-Energy RI beam Productions at CRIB
Direct reactions such as (p,n), (d,p) and (3He,n) in inverse kinematics are mainly used for the production….large cross section
Many RI beams have been produced at CRIB:
typically 104-106 pps
RI beam at CRIB /
Stable nuclei
2013 Dec. 15O
2014 Jan.
10Be

## Slide 6: Cryogenic target: design
Features:
Lq. N2 cooling (automatic refill)
for the better cooling power (~100 W) and thicker target.
Forced target gas flow (>30 l/min) to have a better cooling, and to avoid target thickness reduction by the high-current beam.
Oxygen density monitoring

## Slide 7: Intense secondary beam production using cryogenic gas target
H2 gas target of 760 Torr and 80 mm-long worked at 85K stably for a 7Li2+ beam of 1.3 pμA. (which deposits heat of 7.4W).
Secondary beam: 7Be4+ at 4.0 MeV/u, purity 75% (without degrader/ WF),
  2x108 pps was achieved.
H. Yamaguchi et al., NIMA (2008)
Price of 3He gas became 10 times higher since 2008….a recycling system for 3He gas was built.

## Slide 8: International collaborations at CRIB
CRIB experiments performed in 2007-2011,
by collaborated members of CNS and other institutes:

## Slide 9: Recent research projects (2010-present)
Proton/alpha resonant scattering
  26Si+p (Collaborated with Chung-Ang, Korea) H.S. Jung et al., published at PRC (2012).
  7Li/7Be+a (CNS) H. Yamaguchi et al., PRC (2011&2013).
  21Na+p, 22Na+p [18Ne(a,p), Ne-Na cycle] (IMP/CIAE, China) PRC(2014) & PRC (2013).
  17F+p [Resonances for 14O(a,p)](IMP/CIAE, China)
(α,p) reaction measurement, Active target (GEM-MSTPC)
  18Ne(a,p) (CNS, Hashimoto (now at RCNP))
  30S(α,p) (CNS, Daid Kahl)
  22Mg(α,p) (IOP, Vietnam , Nguyen Ngoc Duy)
  44Ti(a,p) (KEK, Ishiyama) …44Ti beam test successful.
(a,g)
  16N⇒16O*⇒12C+a for 12C(a,g) (Catania, Italy, S. Cherubini) Measurement finished in Sep 2013.
Reaction mechanism
  8B+Pb (Padova, Italy, C. Signorini) Measurement finished in May 2014.
β-decay
  7Be lifetime in metal (Tohoku Univ, Otsuki)

## Slide 10: The thick-target method in inverse kinematics
  Inverse kinematics… measurement is possible for short-lived RI which cannot be used as the target.
  Simultaneous measurement of the excitation function for certain energy range.(Small systematic error, no need to change beam energy.)
  The beam can be stopped in the target…measurement at qcm=180 deg. (where the potential scattering is minimal) is possible.
Measurement of
resonance scattering

## Slide 11: 7Li+a/ 7Be+a study
7Li(a,g)11B …important at high-T, as a production reaction of 11B (the n-process in core-collapse supernovae).
7Be(a,g)11B … one of the reaction in hot p-p chain, relevant at high-T.
a-cluster structure in 11B/11C :
  2a+t / 2a+3He cluster states are known to exist (similar to the dilute cluster structure in 12C.)
  Several “bands” which have a-cluster structure could be formed. We can study the band and cluster structure more in detail.

## Slide 12: 7Be(a,g) in supernovae
np-process calculation (T9>1) shows considerable contribution by 10B(a,p)13C and 7Be(a,g)11C as much as the triple-alpha process.
S. Wanajo et al., Astrophys. J (2010)

## Slide 13: Setup for 7Li/7Be+a
Thick target method with inverse kinematics …An efficient method to measure excitation function.
  7Be beam is monitored by a PPAC (or an MCP detector).
  7Be beam stops in a thick helium gas target (200 mm-long, 1.6 atm).
  Recoiled a particles are detected by DE-E counter (10 mm and 500 mm Si detectors) at forward angle.
  NaI array for g-ray measurement (to identify inelastic events).

## Slide 14: 7Li+a result
Strong alpha resonances were successfully observed, and we determined the a widths (Ga). H. Yamaguchi et al., Phys Rev. C (2011).
T=3/2? 1/2?
Is Jp really 9/2-?
New!

## Slide 15: 7Li+a; results
Resonant reaction rates for the observed resonances are compared with NACRE evaluation (including resonances below 11 MeV).
Conclusion: No need to modify NACRE evaluation (for T9<5).
Newly proposed a negative parity band.
It may not be a simple rotational band, but corresponds to a 2a-t structure [AMD Calc. by Suhara & En’yo]

## Slide 16: Interpretation of the new negative-parity band

## Slide 17: 7Be+a Excitation functions
4 excitation functions… new information on resonant widths, spin, and parity. H. Yamaguchi et al., PRC (2013).

## Slide 18: Resonant contribution to 7Be(a,g)
Small but not negligible contribution compared to lower-lying states (~10%).

## Slide 19: Study on the ap-process
ap-process: (a,p),(p,g) reactions occur faster than β-decay at high temperature. Accelerates the rp-process (Wallace and Woosley, 1981).
Suitable objective for CRIB
  Not many direct measurements of (a,p) reactions have been performed in other facilities.
  Involves A=18-30, proton rich
  unstable nuclei.
  T=1.5GK, close to the
  beam energy at CRIB.
  [See Daid Kahl’s presentation]

## Slide 20
18Ne(a,p) (T. Hashimoto; RCNP)
11C
12C
13C
13N
14N
15N
12N
16O
17O
18O
9C
10C
11N
15O
14O
19F
18F
17F
20Ne
21Ne
22Ne
19Ne
18Ne
stable
unstable
hot-CNO
12C(p, γ)13N(p, γ)14O(b)14N(p, g)15O(b)15N(p, a)12C
second hot CNO cycle
14O(α, p)17F(p, γ)18Ne(b)18F(p, α)15O(b)15O(p, α)12C
18Ne(α, p)21Na
22Na
22Na
23Na
21Na
20Na
18Ne(a, p)21Na is an important breakout reaction from hot-CNO cycle
to the rp-process (B to C in the figure)
A: hot-CNO
B: second hot-CNO
C: 18Ne(a, p)21Na
D: 18Ne(2p, g)20Mg
E: 15O(2p, g)17F
J. Phys. G: Nucl. Part. Phys. 25 (1999)R133
17Ne
X-ray bursts
Relevant energy (temperature):
Ecm = 0.5 - 3.8 MeV (T = 0.6 - 3 GK).
Notes: Explosive hydrogen and helium burning is thought to be the main source of energy generation in novae, X-ray bursts, and also provides an important route for nucleosynthesis of elements up to masses 100 region via the rapid-proton capture process.
This figure shows the estimated temperature and density condition which allow break-out paths to the rp-process from the hot-CNO cycles. Region A characterizes typical condition hot-CNO cycles. Region B indicates the condition of the second hot-CNO cycle. The hot-CNO and the second hot-CNO cycles are linked by the 14O(a, p) reaction. Region C indicates the temperature and density region as which a sufficient reaction flow via 18Ne(a, p)21Na reaction lead to rp-process from the second hot-CNO cycles.
The typical densities in X-ray bursts and nova are estimated in this region.
Therefore, the 18Ne(a, p)21Na reaction is important for break-out to the rp-process from the hot-CNO cycle, which converts the initial CNO elements into heavier elements.
The lowest temperature in Regin C is about 0.6 GK.
In addition, according to some theories, this reaction has important role of the nucleosynthesis in Type II supernovae.
The typical expected temperature region in the type II supernove is 1 to 3 GK.
Therefore, we need the information of reaction cross sections at Ecm =0.5 and 3.8 MeV which corresponds T = 0.6 - 3 GK.

## Slide 21
Experimental Setup
He (90%) +CO2 (10%)
mixture gas(160 torr)
z
x
y
Acts as a He target and a detector (TPC) simultaneously
GEM with “backgammon” type readout pad.
3-dimentional trajectory and energy loss can be measured
⇒ Good event identification.
18Ne beam
Beam monitor

## Slide 22
Typical event of 18Ne(a, p)21Na reaction
Preliminary
Si telescopes
Total energy (MeV)
p
a (Stopped in first layer)
Energy loss in first layer (MeV)
Pad No.
Pad No.
Pad No.
dE/Pad (MeV)
X position (cm)
Y position (cm)
Analysis is in progress …
18Ne
21Na
18Ne
21Na
18Ne
18Ne
18Ne
21Na
18Ne
Preliminary
Reaction events are observed !

## Slide 23: 16N beta-delayed alpha decay
16N→16O*→12C+a decay…carrying information of 12C(a,g) reaction cross section (E1 component) at low energy.
Tang et al. (Argonne)…measurement with 2 ionization chambers. (Low-energy events cannot be detected.)
Using the active target for decay measurement…sensitivity at low-energy events.
Experiment at CRIB proposed by INFN-LNS group (S. Cherubini et al.)

## Slide 24: Performed measurement
Measurement at CRIB performed in Sep. 2013.
RI Beam…16N
  Beam pulsing (on-off) operation by 150-ms interval.
  1-4 x 105 pps after the pulsing, purity 40-80%.
  30-MeV beam injected into the TPC, stopped in the middle of it.
Total 16 days of beamtime, about 2 weeks of data accumulation.
Branching ratio of a-decay…~10-5
⇒ a few decay events /sec.
Pulse shape was recorded by Flash ADC, and the number of injected beam particles was counted by PPAC detectors.

## Slide 25: Typical event (preliminary)
Signals observed in several neighboring channels…candidate of a-decay event.
Event selection by energy and tracking information.

## Slide 26: 21Na/22Na+p experiment
Proton resonant scattering on
21Na: J.J. He, et al., Phys. Rev. C 88, 012801(R) (2013), L.Y Zhang et al., Phys Rev. C 89, 015804 (2014).
Astrophysical reaction 18Ne(a,p)21Na, important breakout reaction in x-ray bursts.
22Na: S. J. Jin, et al, Phys. Rev. C 88, 035801 (2013).
Related to 22Na(p,g) astrophysical reation and Ne-E problem.

## Slide 27: 21Na+p
2x 105 pps 21Na beam was produced with 20Ne primary beam at 8.2 MeV/u and D2 gas (2.9 mg/cm2) target.
21Na Beam was stopped in CH2/C targets and scattered protons were measured with double-sided SSD at forward angles.
Resonances above 8.14MeV…contributes to 18Ne(a,p)21Na
8.385 MeV…new assignment of Jp=1+ (was 2+).

## Slide 28: 8B+Pb; reaction mechanism
Project in collaboration with INFN-LNL (Padova) group (C. Signorini, M. Mazzocco et al.)
Elastic Scattering measurement. Reaction cross section as large as for reactions induced by the 2n-halo 6He.
E.F. Aguilera et al., PRC 79, 021601 (2009)
More recently the fusion cross section for the system 8B + 58Ni has been measured. E.F. Aguilera et al., PRL 107, 092701 (2011)
The sum of the fusion and breakup cross sections exhausts the reaction cross section. V. Guimaraes et al., PRL 84, 1862 (2000)
←RI+Heavy target(Pb/Bi) “reduced” reaction cross section
Measurement at CRIB performed in May, 2014.
8B Beam at CRIB: 50 MeV, 2 x 104 pps on target

## Slide 29: Detector Arrangement
BEAM
TARGET

## Slide 30: ∆E-Eres: Tel. A (θcm = 9° - 47°)
8B
7Be
3He
6Li
4He
H

## Slide 31
Nishina Center, Industrial Cooperation Team http://ribf.riken.jp/sisetu-kyoyo/
Development of a material-wear test with tracer inplanted as an RI beam
－ Industrial use of 7Be beam at E7-CRIB －
To measure surface wear of industrial material
Samples: (part of) engine, bearing, ceramic parts, lubricating oil
Purpose: real-time measurement of wear at the surface (100 μm thickness)
Requirements: long-lived RI (~months) [for off-line measurement]
implant only on the surface with a high density (>100kBq) [for sensitive test ～μm/hour]
Previous method: direct activation
p, d, 3He 10～20MeV, to activate the surface.
 Problem: Must contain nuclides which become long-lived RI.
High heat and radiation damage
RI beam implantation
merit: Independent of composition of samples
low-heat, low-radiation damage
Implantation depth can be adjusted
Achieved: E6-RIPS, 22Na(2.6y) 1.5x108 cps
Two trial beamtimes
Tests in 2012-2013: E7-CRIB, 7Be(53 days) 2x108 cps possible
22Na 3 x 106 pps.
Measure reduction of radiation at the sample,
or increasement of radiation at the oil

## Slide 32: Summary
CRIB is a low-energy RI beam facility in RIBF operated by CNS, University of Tokyo, providing RI beams of good intensity and purity.
Manpower…Minimum to carry out experiments. We are making experiments in a worldwide collaboration with external groups.
Standard experiments: Proton/alpha resonant scattering, direct (a,p) reaction measurement using an active target (GEM-MSTPC)
GEM-MSTPC
  Has been used in several (a,p) measurements, and recently also for alpha decay measurement of 16N.
Resonant elastic scattering
  7Li+a,7Be+a…strong resonances were observed. The “thick target method with inverse kinematics” could be applied to many nuclides. We can study astrophysical reactions and alpha-cluster structures.
  21Na/22Na+p…proton resonant scattering to study astrophysical reactions
Reaction mechanism study
8B+Pb elastic scattering has been measured for studying the reaction mechanism.
We welcome new users and new ideas!