## Slide 1
The Rare RI Ring Facility at RIKEN RI Beam Factory
M. Wakasugi, and Rare RI Ring Collaborators
RIKEN, Nishina Center, Japan
ARIS2014

## Slide 2
Rare RI Ring (R3)
Heavy-ion storage ring dedicated to mass measurement
based on Isochronous Mass Spectrometry
R-process

## Slide 3
SRC
IRC
fRC
RRC
Rilac
ECR
CSM
GARIS
AVF
Rilac2
RIPS
BigRIPS
ZeroDegree
SAMURAI
SHARAQ
Location of R3 in the RIKEN RI Beam Factory
Rare RI Ring
F0: Target
F3: PID & Trigger
SCRIT

## Slide 4
R3: Cyclotron-like Lattice Structure
Injection beam line
Injection septum magnets
Extraction
septum magnets
Sector magnets
Sector magnets
wirh 10 trim coils
Cavity-type
Schottky pickup
Fast-response
Kicker magnets
C-Foil timing detector
(Stop
and PID)
(Start)
Hexagonal-Symmetry
Weak-Focusing Lattice Structure
Circumference : 60.3m
1/6 Optics
Tunes: 1.21 / 0.84
Acceptance :
Momentum DP/P=±0.5%
Transverse 20p / 10p mm mrad

## Slide 5
Isochronous Mass Spectrometry at R3
Two particles with the same momentum have the same flight pass length in the ring
Unknown mass m1 is measured relative to precisely-known reference mass m0
T1 correction factor
Three values T0, T1, and b1 are measured
To make T0 and T1corr values independent of momentum,
highly tuned isochronism in a wide range of momentum is required.

## Slide 6
Uncertainty of m1
b1 Measurement
~ 10-4
Well-known
Reference Mass
~ 10-6
TOF (T0, T1)
Measurement
~ 10-6
T ~ 700ms (2000turns)
dT ~ 100ps
k~10-2
Isochronism of ~10-6 is required during measurement
desired accuracy : dm1/m1 ~10-6

## Slide 7
How to Measure Masses at R3
Precision isochronous field
b1 measurement
From F3 to Start
Start
Stop
T0, T1 measurement
From Start to Stop
PID
2000 turns
accumulation
(~0.7ms)

## Slide 8
Dp/p ±0.5%
T1
T1corr
82Ge
81Ga
80Zn
79Cu
78Ni
○ Many RIs are accepted in the
given machine condition.
○ Isochronism in R3 is tuned for
８0Zn.
○ Some of them are references
for mass determination.
Simulations of 78Ni Mass Measurements at R3
mass references
80Zn
80Zn
T1 correction
78Ni
78Ni

## Slide 9
Reference 80Zn
Rare RI 78Ni
Relation between Mass and
corrected revolution time
Mass
references
Simulations of 78Ni Mass Measurements at R3 II
T0
T1corr
Dm (m1-m0)
dDm

## Slide 10
Status of R3 Construction
1st. Phase (2002~2011)
Design study
R&D study
Ring design was finalized in 2011
2nd. Phase (2012~2013)
Construction budget was approved
Construction was started
Infrastructures, Magnets, Power Supplies,
Control system, Vacuum system, etc.
Each device was tested
3rd. Phase (2014~ )
a-particle transport test
Commissioning using 250MeV p-beam
Upgrading to 6Tm machine
Construction of field-stabilization system
Improving detector system
Short History
We are here
Major Featuers
○ Forming precision isochronous field in 1% momentum range
○ Individual Injection Scheme

## Slide 11
Isochronous Field Formed by 10 Trim Coils
Dp/p=±0.5% &
ex=20pmmmrad
Arc Section
w/ 10 trim coils
w/o trim coil
Re-use of TARN-II Magnets
Laminated sector mag.
15 deg. bending
25 turns coils/pole
with correction coils
3000 A max. current
Added Trim Coils
±60mm
good field region

## Slide 12
Individual Injection Scheme
Kicker
PS
R3
for the effective use of Rare RIs unpredictably produced
Trigger transmission
~ 430 ns
Beam flight time
~ 950 ns
Requirements for Kicker
○ Fast Response < 500 ns
Trigger input
→ Field Activation
○ Being ready to be
activated at any time

## Slide 13
Fast-Response Kicker
Grid-Pulse circuit
PFN
Thyratron
105ns
150ns
Charger (75kV)
Trigger in
Output
Number of kicker 6
Number of cell 13
Impedance 12.5Ω
Capacitance 240pF/cell
Inductance 75nH/cell
Maximum current 3000A/35kV
Magnetic field 0.094T
Kick angle 12.8mrad
Distributed constant type
kicker magnets
Kicker PS
<270ns
<400ns
Trigger
Time (ms)
Magnetic field (G)

## Slide 14
Quick re-charging and Full-Time Charging
PFN charging voltage
Main charger
Sub-charger
Discharge
90%
Hybrid Charging System
to make kicker PS ready for discharge at any time
Charging time 100μs
Wave form of PFN Charging
Main Charger
Half sinusoidal
90% charging
Sub Charger
500kHz
resonance
+10% charging
keep 100±1%
PFN
90%
100%

## Slide 15
Beam Circulation test using a-particles
a-source
foil detector
(Start)
Scintillator
(Stop)
TOF Spectrum for 1 revolution
Trev = 4635.80 (6) ns
Trim field(dB/dr)/B0 = 0.205
at line width minimum (rms 1.7ns)

## Slide 16
Summary
R3 aiming at precision mass measurement is now partially under
construction at RIKEN RIBF.
R3 has a cyclotron based lattice structure for providing
isochronous magnetic field in a wide range of momentum.
Individual injection scheme was established by developing an
ultra-fast response kicker system.
R3 is ready for commissioning experiment, and hopefully mass
measurement will be started in next year.

## Slide 18
Commissioning Experiment using 250MeV p-Beam
p-primary 1-ms pulsed beam
( including 13 micro bunches )
○ Basic Data Acquisition for Ring Operation and Bug-Hunting
○ Ring Operation Sequence Test
Injection ⇨ Accumulation ⇨ Extraction
○ Detector Test
C-Foil Timing Detector and Schottky Pickup
○ Isochronous Tuning Test

## Slide 19
Highly-Sensitive Beam Diagnostic Devices I
Cavity type Schottky pick-up
Resonance frequency 171MHz (TM010)
Harmonic number 57
Tuning range ±0.5MHz
Q0 value 9000(measured)
Shunt impedance 430kΩ (measured)
Gap 40mm
Ceramic tube 290mmΦ, 10mm thickness
Single particle (q>20)
circulation is detectable
expected spectrum for
1000 p-particles in ring
Tuners
Ceramic tube
L-Coupler

## Slide 20
Highly-Sensitive Beam Diagnostic Devices II
C-Foil Timing Monitor
60μg/cm2 C foil
MCP secondary electron detector
Window size : 100×50 mm2
Position sensitivity : less than 10mm
Efficiency : 75 %
Test with 84Kr 200MeV/u
Time resolution 340ps
monitor for first ~1000-turns circulation

## Slide 21
6/6
1/6
5/6
Momentum distribution of a-particles
First confirmation of a-particle one-revolution
Dp/p~6.5%

## Slide 22
Tuning of Isochronism in a-particle test
Expected optimum value
(dB/dr)/B0 = 0.205
Spectral resolution is limited
by current TOF detector
characteristics